## Slide 1: HDMapping v0.92
MapsHD/HDMapping
januszbedkowski@gmail.com

## Slide 2
Data collection
mandeye_raw_data_viewer
QC
QC
Data publication (LAZ)
Ground truth session
Workflow diagram

## Slide 3
Assumptions:
1. Project is composed of multiple sessions
2. Only one session in the project can be „ground truth”
3. multi_session_registration_step_3.exe perfroms pose graph slam
4. It is possible to add Edge for single session (similar to multi_view_tls_registration_step_2.exe)
5. It is possible to add Edge for two different sessions
6. „Ground truth” can not be changed (gizmo is disabled), only multi_view_tls_registration_step_2.exe can change „Ground truth” flag

## Slide 4: IMU versus LiDAR inertial odometry error quality check

## Slide 5
After session load in step2, use show_imu_to_lio_diff to check for large differences between LiDAR and IMU estimations

## Slide 7
WHAT IS SHOWN HERE???

## Slide 8: Georeferencing to ground truth point cloud

## Slide 9: Creating ground truth session from point clouds
1. Using multi_view_tls_registration_step_2.exe
collect ground truth point clouds (laz/las) in one folder
2. Click in menu Create ground truth session from las/laz
3. New session_ground_truth will appear -> use it in step3

## Slide 10: Creating multi session project
1. using multi_session_registration_step_3.exe add session to project
2. Save project
3. Load sessions

## Slide 11: Multi session project – important GUIs
1. downsample point cloud
2. sect sessions to work with (select 1 to work like in step2, select 2 to add Edge between two sessions)
3. select 3 to apply pose graph slam

## Slide 12: Multi session project – create edge for single point cloud
1. Select 1 session
2. Select Manual Loop Closure
3. Choose 2 nodes
4. Click Add Edge

## Slide 13: Multi session project – create edge
1. Select manipulate_active_edge
2. Use ICP to align two point clouds
3. Aplly pose graph slam

## Slide 14: Creating multi session project – save intermediate results
1. Each time you add edge it is advised to save results (two steps)

## Slide 15: Creating multi session project – create edge for two point clouds
1. Select two point clouds
2. Select Manual Loop Closure
3. Add Edge and use ICP to align two point clouds

## Slide 16: Creating multi session project – manual edge alignment with gizmo
1. Use gizmo to align manually if necessary, finally ICP

## Slide 17: Multi session project - final step
1. Publish data using multi_view_tls_registration_step_2.exe (remember to unmark ‚downsample durig load’)

## Slide 18: Multi session project - inspect data in CloudCompare

## Slide 19: Multi session project - inspect data in CloudCompare

## Slide 20: Multi session project - inspect data in CloudCompare

## Slide 21: Multi session project - inspect data in CloudCompare